## Slide 1: Introduction to HPC
HPC Summer School 2016
Claudio Gheller
cgheller@cscs.ch

## Slide 2: School scope, objectives, program
The purpose of the school is to give you an introduction to the the main approaches to exploit modern High Performance Computing systems
    Understand the big picture, the ideas, the concepts
    Understand the programming models
    Experiment specific solutions

## Slide 3: A quick introduction to HPC

## Slide 4: Why HPC…
HPC helps with
Huge data
    Data management in memory
    Data management on disk
Complex problems
    Time consuming algorithms for describing the behavior of a system
    Machine learning
    Data mining and analysis
    Visualization
HPC Requires
Special purpose solutions, in terms of
    Processors
    Networks
    Storage
    Software
    Applications

## Slide 5: HPC systems: the building blocks
C P U
Node
Single powerful processing unit
Multi-core, multi-threaded processor with shared memory
Combination of multi-core processors with NUMA shared memory and shared components

## Slide 6: They need talk to each other…
Node
Network

## Slide 7: …they need also to talk to you…
Storage
User

## Slide 8: Issues and limitations: a matter of money…
…because money matters: HPC systems are expensive!
    Power consumption
    Cooling and infrastructural costs
    Costs of technology:
      Speed-up the processor
      Increase network bandwidth
      Reduce latencies
      Improve connectivity
      Make I/O faster
      …

## Slide 9: Example: HPC systems power consumption
Coming HPC systems are anticipated to draw enormous amounts of electrical power…
Example: N.1 Top 500
Year (Nov.) | System | Performance(Tflop/s) | Electrical power (KW)
2002 | Hearth Simulator | 41 | 3200
2005 | Blue Gene/L | 367 | 1433
2008 | Roadrunner | 1105 | 2483
2009 | Jaguar | 2331 | 6950
2011 | K computer | 11280 | 12659
2012 | Titan | 27112 | 8209
2014 | Tianhe-2 | 54902 | 17808
2020 | ???????? | 1000000 | >100000 (100 MW!!!)
THIS IS NOT SUSTAINABLE!!!

## Slide 10: The end of the “Free Performance Lunch” era
Moore’s Law does not help anymore in increasing the performance
Clock speed cannot increase more:
heat (too much of it and too hard to dissipate)
current leakage
power consumption (too high – also memory must be considered!!!)
Notes: However, below 90 nm, the static power dissipation (power lost due to
current leakage through the silicon substrate) has overtaken
dynamic power dissipation. This leads to a stall in clock fre-
quency improvements in order to stay within practical ther-
mal power dissipation limits.

## Slide 11: Improving efficiency: the advent of accelerators
Node
Network

## Slide 12: Why accelerators help
A few main reasons:
lower frequencies of GPU clocks
more of the transistors in a gpu are actually working on the computation. CPUs are more general purpose. They require energy to support such “flexibility”
Single Instruction Multiple Data (SIMD) approach, which leads to a simpler architecture and instruction set

## Slide 13: Piz Daint
“Piz Daint” CRAY XC30 system @ CSCS
(N.6 in Top500)
Nodes:
5272 CPUs 8-core Intel SandyBridge equipped with:
32 GB DDR3 memory
One NVIDIA Tesla K20X GPU with 6 GB of GDDR5 memory
Overall system
42176 cores and 5272 GPUs
170+32 TB
Interconnect: Aries routing and communications ASIC, and dragonfly network topology
Peak performance: 7.787 Petaflops
User Lab:
    http://www.cscs.ch/user_lab/becoming_a_user/index.html

## Slide 14: Efficiency comparison
Data from last Top500 (June 2016)
System | RPEAK (TFlop/sec) | Power (MW) | Efficiency (MF/sec/W)
Piz Daint (GPU - 8) | 7788 | 2.325 | 3349
Thiane-2 (MIC - 1) | 54902 | 17.808 | 3083
Titan (GPU - 2) | 27112 | 8.209 | 3302
Sequoia (BGQ - 4) | 20132 | 7.890 | 2551
K computer (Sparc - 5) | 11280 | 12.66 | 891
Mira (BGQ – 6) | 10066 | 3945 | 2551

## Slide 15: Programming Models
Distributed Memory domain
Message passing: MPI
Other approaches:
coarrays, UPC…
Message/Task driven:
Charm++, HPX…
Shared memory,
Multi-threads domain:
OpenMP, pthreads,
C++11…
Accelerator domain:
CUDA, OpenCL, OpenACC, OpenMP, OpenGL…

## Slide 16: Week 1: MPI & OpenMP

## Slide 17: Week 2: GPU programming

## Slide 18: BOF
JULY 20 (wed.) A.Ziegler, P.Lenarczyk:
Quantum transport in nanoelectronic devices
JULY 21 (thurs.) M.Beseda, J.Kruzik:
Energy consumption optimization of the Total-FETI solver
JULY 26 (tue.) M.Zacharias
Raptr – Parallel implementation of an iterative reconstruction algorithm
Free slots still available! Other seminars are welcome!!!

## Slide 19: The Team
Claudio Gheller – School coordinator (everyday), MPI I/O (Thursday first week)
Ben Cumming – OpenMP, CUDA (mon., tue., first week; mon., tue., second week)
Karakasis Vasileios – Tools and practicals (first week), OpenACC (wed. second week)
Maxime Martinasso – MPI (wed., thur., first week)
Jean Favre – Visualization (fri., first week)
Radim Janalík – Practicals (everyday)
Juraj Kardos – Practicals (everyday)
Andreas Jocksch – Practicals (second week)
Patrick Sanan – Scientific Libraries (thur., second week)
Tatjana Ruefli – Event manager (on call)